Lecture 3
Fundamental Limitations of Solar Cells
R. Treharne
Nov 5th 2014

---
L3
Key Question
Why can't a solar cell have a 100% efficiency?
(Or even close to 100%?)
You should be able to answer this question after this lecture

---
Lecture Outline
Black Body Radiation
Absorbtion and radiative recombination
Detailed Balance
The Shockley-Queisser Limit
Requirements for real physical systems
Review of real PV device efficiencies
Exceeding the SQ limit (funky solar)

---
Black Body Radiation
A black body absorbs all radiation regardless of frequency or angle of incidence.
A black body in thermal equilibrium emits radiation according to Planck's Law.

---
Planck's Law
Photon Flux – Number of photons of energy E per unit area per second
b( E )={ 2F }over{ h^{3}c^{2} }left( {E^{2}} over {e^{E/k_{B}T}-1}right )
Units – Number of photons of energy E per unit area per second

---
Planck's Law
Photon Flux density from a spherical black body
b( E )={ 2F }over{ h^{3}c^{2} }left( {E^{2}} over {e^{E/k_{B}T}-1}right )
Look familiar?
c.f. Ideal diode
Units – Number of photons of energy E per unit area per second

---
Planck's Law
Photon Flux – Number of photons of energy E per unit area per second
b( E )={ 2F }over{ h^{3}c^{2} }left( {E^{2}} over {e^{E/k_{B}T}-1}right )
What the heck is this?
Units – Number of photons of energy E per unit area per second

---
Planck's Law
F = %pi sin^{ 2 }{ %theta }
Geometrical factor
B
%theta_{ B }
A
F_{ A }=%pi
F_{ A }=%pi
F_{ B }=%pi sin^{ 2}(%theta_{B})

---
Irradiance
Irradiance - Emitted energy flux density
L(E) = Eb(E)
This is what solar spectrum data is measured in

---
Irradiance
Irradiance - Emitted energy flux density
L(E) = Eb(E)
This is what solar spectrum data is measured in
Power Density given by
P = int^{infty}_{0}L(E)dE

---
Irradiance
Irradiance - Emitted energy flux density
L(E) = Eb(E)
This is what solar spectrum data is measured in
Stefan-Boltzmann Law
Power Density given by
P = int^{infty}_{0}L(E)dE = %sigma_{ s }T^{ 4 }
%sigma_{ S }={2%pi^{ 5 }k_{B}^{ 4 }}over{ 15c^{2}h^{3} }
Stefan's constant

---
The Sun (again)