Lecture 3
Fundamental Limitations of Solar Cells
R. Treharne
Nov 5th 2014

---
L3
Key Question
Why can't a solar cell have a 100% efficiency?
(Or even close to 100%?)
You should be able to answer this question after this lecture

---
Lecture Outline
Black Body Radiation
Absorbtion and radiative recombination
Detailed Balance
The Shockley-Queisser Limit
Requirements for real physical systems
Review of real PV device efficiencies
Exceeding the SQ limit (funky solar)

---
Black Body Radiation
A black body absorbs all radiation regardless of frequency or angle of incidence.
A black body in thermal equilibrium emits radiation according to Planck's Law.

---
Planck's Law
Photon Flux – Number of photons of energy E per unit area per second
b( E )={ 2F }over{ h^{3}c^{2} }left( {E^{2}} over {e^{E/k_{B}T}-1}right )
Units – Number of photons of energy E per unit area per second

---
Planck's Law
Photon Flux density from a spherical black body
b( E )={ 2F }over{ h^{3}c^{2} }left( {E^{2}} over {e^{E/k_{B}T}-1}right )
Look familiar?
c.f. Ideal diode
Units – Number of photons of energy E per unit area per second

---
Planck's Law
Photon Flux – Number of photons of energy E per unit area per second
b( E )={ 2F }over{ h^{3}c^{2} }left( {E^{2}} over {e^{E/k_{B}T}-1}right )
What the heck is this?
Units – Number of photons of energy E per unit area per second

---
Planck's Law
F = %pi sin^{ 2 }{ %theta }
Geometrical factor
B
%theta_{ B }
A
Black body
F_{ A }=%pi
F_{ A }=%pi
F_{ B }=%pi sin^{ 2}(%theta_{B})

---
Irradiance
Irradiance - Emitted energy flux density
L(E) = Eb(E)
This is what solar spectrum data is measured in

---
Irradiance
Irradiance - Emitted energy flux density
L(E) = Eb(E)
This is what solar spectrum data is measured in
Power Density given by
P = int^{infty}_{0}L(E)dE

---
Irradiance
Irradiance - Emitted energy flux density
L(E) = Eb(E)
This is what solar spectrum data is measured in
Stefan-Boltzmann Law
Power Density given by
P = int^{infty}_{0}L(E)dE = %sigma_{ s }T^{ 4 }
%sigma_{ S }={2%pi^{ 5 }k_{B}^{ 4 }}over{ 15c^{2}h^{3} }
Stefan's constant

---
Detailed Balance

---
Detailed Balance

---
Detailed Balance

---
Two Band System

---
Two Band System

---
Two Band System

---
Two Band System

---
Requirements for ideal PV devices

---
Real World Device Limitations

---
Real World Device Limitations

---
Real World Device Limitations

---
Real World Device Limitations

---
Real World Device Limitations

---
The Sun (again)
The sun is a black body emitter with a temperature of 5760K
At its surface, the Power density is:
       PS = 62 MW m-2
what is the power density of the Sun's emitted radiation at the Earth's surface, PE?
P_{ E } = F_{ E } over F_{ S }P_{ S }
        ~ 1353 m-2

---
Beating the SQ limit
Tandem Cells
Multi-junctions
Concentrator PV
Thermoelectric PV
Hot Carrier solar cells

---
Beating the SQ limit

---
Tandem Cells
Tandem Cells
Why have one junction when you can have two?
GaAs/InGaP
T. Takamoto et. al. “Over 30% Efficient InGaP/GaAs tandem solar cells”, APL, 70 381 (1997)

---
Tandem Cells
Detailed balance calculations for two band gap system:
Maximum theoretical efficiency ~ 46%

---
Tandem Cells
Disadvantages of tandems based on III-V's
High precision fabrication required
Materials balance (tunnel junction)
High cost (materials + deposition)
Not practical for concentrator systems
Are there other strategies?

---
Tandem Cells
Inorganic/Organic Hybrid Tandems
Cheap
Easy to make (non-vacuum dep)
Can apply to existing Si technology
Watch this space
c-Si efficiency boosted by 20% (by using perovskites)

---
Multi-junctions
Why have two junctions when you can have three (or more)?
Ge/InGaAs/InGaP – Max η ~ 35%

---
Multi-junctions
44.7%!
Four junction cell based on III-V
Fraunhofer Institute

---
Multi-junctions
S. P. Bremner et. al. Prog. PV. 16:225-233 (2008)

---
Concetrators
Increase photon flux increase efficiency
Theoretical prediction for two junction system @ T = 320K

---
Concentrators
Fresnel Lenses
200 – 300 suns
1 axis tracking

---
Parabolic Mirror Array
~ 500 suns
25kW output
2 axis tracking